## Slide 1: Introduction to Data communication

## Slide 2: agenda
Data and Information
Data communication
Characteristics of Data Communication
Components of Data Communication
Data representation

## Slide 3: Data and Information Data refers to the raw facts that are collected while information refers to processed data that enables us to take decisions.

## Slide 4: DATA COMMUNICATION
Data Communication is a process of exchanging data or information
In case of computer networks this exchange is done between two devices over a transmission medium.

## Slide 5: Characteristics of Data Communication
The effectiveness of any data communications system depends upon the following four fundamental characteristics:
Delivery: The data should be delivered to the correct destination and correct user.
Accuracy: The communication system should deliver the data accurately, without introducing any errors. The data may get corrupted during transmission affecting the accuracy of the delivered data.
Timeliness: Audio and Video data has to be delivered in a timely manner without any delay; such a data delivery is called real time transmission of data.
Jitter: It is the variation in the packet arrival time. Uneven Jitter may affect the timeliness of data being transmitted

## Slide 6: Components of Data Communication
A Data Communication system has five components

## Slide 7
Message: Message is the information to be communicated by the sender to the receiver.
Sender: The sender is any device that is capable of sending the data (message).
Receiver: The receiver is a device that the sender wants to communicate the data (message).
Transmission Medium: It is the path by which the message travels from sender to receiver.
It can be wired or wireless and many subtypes in both.
Protocol: It is an agreed upon set or rules used by the sender and receiver to communicate data.

## Slide 8: Protocals
It is an agreed upon set or rules used by the sender and receiver to communicate data. A protocol is a set of rules that governs data communication.
A Protocol is a necessity in data communications without which the communicating entities are like two persons trying to talk to each other in a different language without know the other language.
The key features of a protocol are:
  •Syntax – format of data blocks
  •Semantics – control information for coordination and error handling
  •Timing – speed matching and sequencing

## Slide 9: DATA REPRESENTATION
There may be different forms in which data may be represented.
Some of the forms of data used in communications are as follows:
1.Text:Text includes combination of alphabets in small case as well as upper case. It is stored as a pattern of bits. Prevalent encoding system : ASCII, Unicode
2. Numbers: Numbers include combination of digits from 0 to 9. It is stored as a pattern of bits. Prevalent encoding system : ASCII, Unicode
3. Images: An image is worth a thousand words‖ is a very famous saying.
4. Audio: Data can also be in the form of sound which can be recorded and broadcasted
5. Video: Video refers to broadcasting of data in form of picture or movie

## Slide 10: Thank you
Alex Sangi
alexander.sangi@nit.go.tz

## Slide 11: Data and Signal

## Slide 12: agenda
Signal
Characteristics of a Signal
Signal Type
Periodic & Non Periodic Signals
Analog signal
Characteristics of an Analog Signal
Digital Signal
Transmission Impairment

## Slide 13
Computer networks are designed to transfer data from one point to another. During transit data is in the form of electromagnetic signals. Hence it is important to study data and signals before we move to further concepts in data communication.

## Slide 14: Signal
A signal is essentially any detectable physical quantity that carries information from one point (the source) to another (the receiver). Think of it as the carrier or the messenger of a piece of data.

## Slide 15
Characteristics of a Signal
It has to be a physical phenomenon that can vary in time or space.
The variation is what represents the information.
It must be able to travel through a medium (like air, wire, or fiber optic cable).

## Slide 16
Signal Type | Physical Quantity | Information Carried
Sound Signal | Variations in air pressure (vibrations) | A person's voice, music, or a car horn
Electrical Signal | Variations in voltage or current | Your voice traveling through a telephone wire or data moving on a computer cable
Light Signal | Variations in light intensity | Flashes from a lighthouse, or data traveling through a fiber optic cable
Radio Signal | Variations in electromagnetic waves | Music broadcast from a radio station or your phone's connection to a tower

## Slide 17: Encoding
Encoding is the process of converting information into a specific format (the signal) so it can be reliably transmitted or stored. It's like translating a message from one language (the raw data) into a standardized code (the signal) that the receiver can understand and convert back.
The main purpose of encoding is to make the information suitable for the chosen transmission medium and to ensure it's robust against errors.

## Slide 18: DATA & SIGNALS
Data can be Analog or Digital.
Analog data refers to information that is continuous; ex. sounds made by a human voice
Digital data refers to information that has discrete states. Digital data take on discrete values. For example, data are stored in computer memory in the form of Os and 1s

## Slide 19: Types of signal
Signals can be of two types:
  Analog Signal: They have infinite values in a range.
  Digital Signal: They have limited number of defined values

## Slide 20: Periodic & Non Periodic Signals
Signals which repeat itself after a fixed time period are called Periodic Signals.
Signals which do not repeat itself after a fixed time period are called Non-Periodic Signals.
In data communications, we commonly use periodic analog signals and non-periodic digital signals.

## Slide 21: ANALOG SIGNAL
An Analog Signal is a continuous, smooth wave that perfectly mirrors a real-world physical change, like sound, light, or temperature.
The core idea is continuity. There are no sudden jumps or steps; the value can be anything within a given range, just like things in the natural world.

## Slide 22: ANALOG SIGNAL
An analog signal has infinitely many levels of intensity over a period of time.
As the wave moves from value A to value B, it passes through and includes an infinite number of values along its path as it can be seen in the figure below.
A simple analog signal is a sine wave that cannot be further decomposed into simpler signals.

## Slide 23: Characteristics of an Analog Signal
Peak Amplitude
  The amplitude of a signal is the absolute value of its intensity at time t
  The peak amplitude of a signal is the absolute value of the highest intensity.
  The amplitude of a signal is proportional to the energy carried by the signal

## Slide 24: Characteristics of an Analog Signal ……..
2. Frequency
Frequency refers to the number of cycles completed by the wave in one second.
Period refers to the time taken by the wave to complete one cycle.
Frequency & Period are inverse of each other.

## Slide 25
Example1. A wave has a frequency of 100hz. Its period(T) is given by
T = 1/ F = 1/ 100 = 0.01 sec
Example2. A wave completes its one cycle in 0.25 seconds. Its frequency is given by
F = 1 / T = 1 / 0.25 = 4 Hz

## Slide 26: Characteristics of an Analog Signal ……..
3. Phase
Phase describes the position of the waveform with respect to time (specifically relative to time O).
Phase indicates the forward or backward shift of the waveform from the axis
It is measured in degrees or radian

## Slide 27: Wavelength
The wavelength of a signal refers to the relationship between frequency (or period) and propagation speed of the wave through a medium.
The wavelength is the distance a signal travels in one period.
It is given by
Wavelength = Propagation Speed X Period OR
Wavelength =Propagation Speed X 1/Frequency
It is represented by the symbol : λ (pronounced as lamda) It is measured in micrometers
It varies from one medium to another.

## Slide 28: Time Domain and Frequency domain representation of signals
A sine wave can be represented either in the time domain or frequency domain.
The time-domain plot shows changes in signal amplitude with respect to time. It indicates time and amplitude relation of a signal.
The frequency-domain plot shows signal frequency and peak amplitude.

## Slide 29: Composite Signal
A composite signal is a combination of two or more simple sine waves with different frequency, phase and amplitude.
If the composite signal is periodic, the decomposition gives a series of signals with discrete frequencies; if the composite signal is non-periodic, the decomposition gives a combination of sine waves with continuous frequencies.

## Slide 30
For data communication a simple sine wave is not useful, what is used is a composite signal which is a combination of many simple sine waves.
According to French Mathematician, Jean Baptist, any composite signal is a combination of simple sine waves with different amplitudes and frequencies and phases.
Composite signals can be periodic or non periodic.
A periodic composite signal can be decomposed into a series of signals with discrete frequencies.
A non-periodic signal when decomposed gives a combination of sine waves with continuous frequencies.

## Slide 31: Digital Signal
A digital is a signal that has discrete values.
The signal will have value that is not continuous.
Information can also be explained in the form of a digital signal.
LEVEL
Information in a digital signal can be represented in the form of voltage levels.
Ex. In the signal shown below, a ‗1‘ is represented by a positive voltage and a ‗0‘ is represented by a Negative voltage.

## Slide 32: A digital signal with four levels
In general, if a signal has L levels then, each level need Log2L bits
Example: Consider a digital Signal with four levels, how many bits are required per level? Answer: Number of bits per level = Log2L = Log24 = 2
Hence, 2 bits are required per level for a signal with four levels.

## Slide 33
BIT LENGTH or Bit Interval (Tb)
It is the time required to send one bit.
It is measured in seconds.
BIT RATE
It is the number of bits transmitted in one second.
It is expressed as bits per second (bps).
Relation between bit rate and bit interval can be as follows
Bit rate = 1 / Bit interval
BAUD RATE
It is the rate of Signal Speed, i.e the rate at which the signal changes.
It is the number of symbols per second
A digital signal with two levels ‗0‘ & ‗1‘ will have the same baud rate and bit rate.

## Slide 34
The diagram below shows three signal of period (T) 1 second
      Signal with a bit rate of 8 bits/ sec and baud rate of 8 baud/sec
      Signal with a bit rate of 16 bits/ sec and baud rate of 8 baud/sec
      Signal with a bit rate of 16 bits/ sec and baud rate of 4 baud/sec

## Slide 35: Transmission Impairment
In communication system, analog signals travel through transmission media, which tends to deteriorate the quality of analog signal, which means that the signal at the beginning of the medium is not the same as the signal at the end of the medium.
The imperfection causes signal impairment

## Slide 36: Causes of impairment

## Slide 37: Attenuation
It means loss of energy.
The strength of signal decreases with increasing distance which causes loss of energy in overcoming resistance of medium.
This is also known as attenuated signal.
Amplifiers are used to amplify the attenuated signal which gives the original signal back and compensate for this loss.

## Slide 38
Attenuation is measured in decibels(dB). It measures the relative strengths of two signals or one signal at two different point.
Attenuation(dB) = 10log10(P2/P1)

## Slide 39: Distortion
It means changes in the form or shape of the signal.
This is generally seen in composite signals made up with different frequencies.
Each frequency component has its own propagation speed travelling through a medium. And thats why it delay in arriving at the final destination Every component arrive at different time which leads to distortion.
Therefore, they have different phases at receiver end from what they had at senders end.

## Slide 40: Noise
The random or unwanted signal that mixes up with the original signal is called noise.
There are several types of noise such as induced noise, crosstalk noise, thermal noise and impulse noise which may corrupt the signal.
Induced noise comes from sources such as motors and appliances.
Thermal noise is movement of electrons in wire which creates an extra signal.
Crosstalk noise is when one wire affects the other wire.
Impulse noise is a signal with high energy that comes from lightning or power lines

## Slide 41
The signal-to-noise ratio is defined as
SNR = AVG SIGNAL POWER / AVG NOISE POWER
SNRdB = 10Log10SNR
EXAMPLE
The values of SNR and SNRdB for a noiseless channel are
SNR = Signal Power/0 = ∞
SNRdB = 10Log10 ∞ = ∞
We can never achieve this ratio in real life ; it is an ideal.

## Slide 42: SIGNAL ENCODING

## Slide 43: SIGNAL ENCODING
Data can be analog or digital, so can be the signal that represents it.
Signal encoding: is the conversion from analog/digital data to analog / digital signal.
The possible encodings are:
Digital data to Digital Signal
Digital data to Analog Signal
Analog data to Digital Signal
Analog data to Analog Signal

## Slide 44: SYNCHRONIZATION
In order to receive the signals correctly, the receivers bit intervals must correspond exactly to the senders bit intervals.
The clock frequency of the transmitter and receiver should be the same.
If the clock frequency at the receiver is slower or faster than the bit intervals are not matched and the received signal is different than the transmitted one.

## Slide 45: Digital Data to Digital Signal
Coding methods Coding methods are used to convert digital data into digital signals.
There are two types of coding methods:
Line Coding
Block Coding
Line Encoding
It is the process of converting Digital data into digital signal.
In other words, it is converting of binary data(i.e. A sequence of bits) into digital signal (i.e. a sequence of discrete, discontinuous voltage pulses)

## Slide 46: Classification of Line Codes

## Slide 47
Unipolar: All signal levels are either above or below the time axis.
NRZ - Non Return to Zero scheme is an example of this code. The signal level does not return to zero during a symbol transmission.
Polar
NRZ-voltages are on both sides of the time axis
Polar NRZ scheme can be implemented with two voltages. E.g. +V for 1 and -V for 0.

## Slide 48
There are two variations:
NZR - Level (NRZ-L) - positive voltage for one symbol and negative for the other
NRZ - Inversion (NRZ-I) - the change or lack of change in polarity determines the value of a symbol. E.g. a ―1‖ symbol inverts the polarity a ―0‖ does not.

## Slide 49
Polar – RZ
The Return to Zero (RZ) scheme uses three voltage values. +, 0, -.
Each symbol has a transition in the middle. Either from high to zero or from low to zero
More complex as it uses three voltage level. It has no error detection capability

## Slide 50: Polar - Biphase: Manchester and Differential Manchester
Manchester coding is a combination of NRZ-L and RZ schemes.
Every symbol has a level transition in the middle: from high to low or low to high. It uses only two voltage levels.
Differential Manchester coding consists of combining the NRZ-I and RZ schemes.
Every symbol has a level transition in the middle. But the level at the beginning of the symbol is determined by the symbol value. One symbol causes a level change the other does not.

## Slide 51: Data Transmission

## Slide 52
Data transmission is the process of moving data from a sender to a receiver through a transmission medium, which can be physical (guided) or wireless (unguided).
Key aspects include the direction of transmission (simplex, half-duplex, or full-duplex), the method of transfer (serial or parallel), and ensuring data integrity through error detection and control.
Essential concepts also include signal properties like amplitude, frequency, and phase, along with factors like attenuation, distortion, and noise that can affect signal quality.

## Slide 53: direction of transmission
Two devices communicate with each other by sending and receiving data. The data can flow between the two devices in the following ways.
  1.Simplex
  2.Half Duplex
  3.Full Duplex

## Slide 54: Simplex
In Simplex, communication is unidirectional
Only one of the devices sends the data and the other one only receives the data.
Example: in the diagram: a cpu send data while a monitor only receives data.

## Slide 55: Half Duplex
In half duplex both the stations can transmit as well as receive but not at the same time.
When one device is sending other can only receive and viceversa (as shown in figure above.)
Example: A walkie-talkie.

## Slide 56: Full Duplex
In Full duplex mode, both stations can transmit and receive at the same time.
Example: mobile phones

## Slide 57: TRANSMISSION MEDIA
A transmission medium can be broadly defined as anything that can carry information from a source to a destination.
For example, the transmission medium for two people having a dinner conversation is the air.
For a written message, the transmission medium might be a mail carrier, a truck, or an airplane.
The transmission medium is usually free space, metallic cable, or fiber-optic cable.

## Slide 58: Guided Media
Guided media, which are those that provide a conduit from one device to another, include twisted-pair cable, coaxial cable, and fiber-optic cable.
A signal traveling along any of these media is directed and contained by the physical limits of the medium.
Twisted-pair and coaxial cable use metallic (copper) conductors that accept and transport signals in the form of electric current.
Optical fiber is a cable that accepts and transports signals in the form of light

## Slide 59: Twisted-Pair Cable
A twisted pair consists of two conductors (normally copper), each with its own plastic insulation, twisted together.
One of the wires is used to carry signals to the receiver, and the other is used only as a ground reference.
Twisted-pair cables are used in telephone lines to provide voice and data channels.
Local-area networks, such as lOBase-T lOOBase-T, 1G and 10G also use twisted-pair cables.

## Slide 60: Coaxial Cable
Coaxial cable (or coax) carries signals of higher frequency ranges than those in twisted pair cable, in part because the two media are constructed quite differently.
Instead of having two wires, coax has a central core conductor of solid or stranded wire (usually copper) enclosed in an insulating sheath, which is, in turn, encased in an outer conductor of metal foil, braid, or a combination of the two.
The outer metallic wrapping serves both as a shield against noise and as the second conductor, which completes the circuit.

## Slide 61: Fiber Optic Cable
A fiber-optic cable is made of glass or plastic and transmits signals in the form of light.
To understand optical fiber, we first need to explore several aspects of the nature of light.
Light travels in a straight line as long as it is moving through a single uniform If a ray of light traveling through one substance suddenly enters another substance (of a different density), the ray changes direction.
Fiber-optic cable is often found in backbone networks because its wide bandwidth is costeffective. Today, with wavelength-division multiplexing (WDM), we can transfer data at a rate of 1600 Gbps. The SONET network provides such a backbone .

## Slide 62: Advantages of Fiber cable
Higher bandwidth.: Currently, data rates and bandwidth utilization over fiber-optic cable are limited not by the medium but by the signal generation and reception technology available.
Less signal attenuation: A signal can run for 50 km without requiring regeneration. We need repeaters every 5 km for coaxial or twisted-pair cable.
Immunity to electromagnetic interference. Electromagnetic noise cannot affect fiber- optic cables.
Resistance to corrosive materials. Glass is more resistant to corrosive materials than copper.
Light weight. Fiber-optic cables are much lighter than copper cables.
Greater immunity to tapping. Fiber-optic cables are more immune to tapping than copper cables.

## Slide 63: DiSadvantages of fiber cable

## Slide 64: UNGUIDED MEDIA: WIRELESS
Unguided media transport electromagnetic waves without using a physical conductor.
This type of communication is often referred to as wireless communication.

## Slide 65
Signals are normally broadcast through free space and thus are available to anyone who has a device capable of receiving them.
Unguided signals can travel from the source to destination in several ways:
  ground propagation,
  sky propagation, and
  line-of- sight propagation.

## Slide 66: Radio Waves
Waves ranging in frequencies between 3 kHz and 1 GHz are called radio waves.
Radio waves, for the most part, are omnidirectional.
When an antenna transmits radio waves, they are propagated in all directions.
This means that the sending and receiving antennas do not have to be aligned.
A sending antenna sends waves that can be received by any receiving antenna.
The omnidirectional characteristics of radio waves make them useful for multicasting, in which there is one sender but many receivers. AM and FM radio, television, maritime radio, cordless phones, and paging are examples of multicasting.

## Slide 67: Microwaves
Electromagnetic waves having frequencies between I and 300 GHz are called microwaves. Microwaves are unidirectional.
When an antenna transmits microwave waves, they can be narrowly focused.
This means that the sending and receiving antennas need to be aligned.
The unidirectional property has an obvious advantage.

## Slide 68: Infrared
Infrared waves, with frequencies from 300 GHz to 400 THz (wavelengths from 1 mm to 770 nm), can be used for short-range communication.
Infrared waves, having high frequencies, cannot penetrate walls.
This advantageous characteristic prevents interference between one system and another; a short-range communication system in one room cannot be affected by another system in the next room.

## Slide 69: Switching Techniques in Data Communication

## Slide 70: Lecture Objectives
By the end of this lecture, students should be able to:
Define circuit switching, packet switching, and message switching.
Explain the working principles of each switching technique.
Identify and discuss real-world applications where these switching methods are used.
Compare the merits and limitations of each switching technique.

## Slide 71: switching technique
In data communication, a switching technique is the method used to move data from a sender to a receiver through a network.
Because devices in a network are not always directly connected, switching determines how data is transmitted, routed, and delivered across various intermediate nodes (switches or routers).
Switching technique is the way a network chooses a path and transfers data between two communicating devices.
Switching techniques are important because they allow networks to share communication channels, reduce costs, and improve efficiency.

## Slide 72: Main Switching Techniques in Data Communication
1. Circuit Switching
A dedicated communication path is established between sender and receiver before data transfer begins. Works like a traditional telephone call.
2. Packet Switching
Data is broken into small packets, and each packet is transmitted independently across the network. Used in the Internet.
3. Message Switching
Entire messages are transferred from node to node using a store-and-forward mechanism. No dedicated path is required.

## Slide 73: 1. Circuit Switching
A switching method where a dedicated communication path is established between the source and destination before data transfer begins.
Used in traditional telephony networks.
The path remains exclusively reserved for the duration of the communication session.

## Slide 74: Circuit Switching – Working Principle
Connection Establishment
  A dedicated circuit is set up between sender and receiver through the network switches.
Data Transfer
  Once established, data flows continuously without interruption.
  No addressing needed during data transfer.
Connection Termination
  Circuit is released after communication ends.
Key Characteristics:
Guaranteed bandwidth
Real-time data flow
Inefficient if the channel remains idle

## Slide 75: Applications of Circuit Switching
Traditional telephone systems (PSTN)
Voice communication requiring real-time transmission
Video conferencing in older systems

## Slide 76: Advantages and Disadvantages of Circuit
Advantages:
Guaranteed bandwidth
No congestion once circuit is established
Suitable for real-time communication
Disadvantages:
Wastes bandwidth during idle times
Long setup time
Inefficient for bursty data traffic

## Slide 77: 2. Packet Switching
Data is broken into smaller packets, each containing a portion of the message along with control information.
Packets travel independently through the network and may take different paths to reach the destination.
Used widely in modern data networks including the Internet.

## Slide 78: Packet Switching – Working Principle
Message Splitting
  Data is divided into packets.
Independent Routing
  Each packet is routed separately based on destination address.
Packet Reassembly
  The receiving device reassembles packets using sequence numbers.
Two Types:
Datagram Packet Switching: Each packet is treated independently.
Virtual Circuit Packet Switching: A logical path is established first.
Key Characteristics:
Efficient use of network resources
Supports bursty traffic
Packets may arrive out of order

## Slide 79: Applications of Packet Switching
Internet and IP networks
Email communication
Browsing and social media
VoIP (Voice over IP)
Multimedia streaming
Cloud and data center networks

## Slide 80: Advantages and Disadvantages of Packet Switching
Advantages:
Efficient use of network bandwidth
Supports many users simultaneously
Robust – packets can take alternative routes
Ideal for data, multimedia, and Internet traffic
Disadvantages:
Possible delay and jitter
Packets may arrive out of order
Requires complex protocols and error control

## Slide 81: Message Switching
Entire messages are sent as a single unit and stored temporarily at intermediate nodes (store-and-forward).
No dedicated path is required.
Messages may experience delays depending on network traffic and storage availability.

## Slide 82: Message Switching – Working Principle
Message Creation
  The entire message is prepared as one block.
Store and Forward
  Each intermediate node stores the entire message before forwarding it.
Delivery
  Message reaches destination after passing through several nodes.
Key Characteristics:
No need for a dedicated path
High delay for large messages
Suitable for non-real-time communication

## Slide 83: Applications of Message Switching
Telegraph networks
Early postal-type data networks
Military communication systems
Store-and-forward email systems (historically)

## Slide 84: Advantages and Disadvantages of Message Switching
Advantages:
No need for a dedicated circuit
Better bandwidth use compared to circuit switching
Provides store-and-forward flexibility
Disadvantages:
High delay due to entire message storage
Requires large storage at intermediate nodes
Not suitable for real-time communication (voice/video)

## Slide 85: wireless technologies in mobile data communications

## Slide 86
Wireless technologies have transformed the way people, devices, and systems communicate in the modern digital world.
Unlike traditional wired communication, wireless communication uses electromagnetic waves—such as radio, infrared, or microwave signals—to transmit data over the air.
Mobile data communication, a core component of wireless technology, refers to the transmission of digital data across mobile networks using portable devices such as smartphones, tablets, laptops, sensors, and IoT devices.

## Slide 87: WAP & WAE Concepts
Wireless Application Protocol (WAP)
A suite of protocols enabling mobile devices to access internet content and data exchange.
It is device independent and network independent
Uses a lightweight request/response model similar to HTTP.
WAP stack resembles the OSI model but is optimized for wireless networks.

## Slide 88: WAP Architecture
WAP is essentially a set of protocols designed to bridge the gap between the mobile world (devices with limited capabilities like older cell phones) and the internet.
It's like a simplified, compact version of the standard internet (TCP/IP) protocol stack, optimized for low bandwidth and limited display screens.

## Slide 89: The Five WAP Layers and Protocols
Application Layer (WAE)
Session Layer (WSP)
Transaction Layer (WTP)
Security Layer (WTLS)
Transport Layer (WDP)
Bearer GSM IS:136 CDMA PHS

## Slide 90: 1. Application Layer (WAE)
Protocol: Wireless Application Environment (WAE)
Function: This is the top-most layer, responsible for providing the services that users directly interact with.
It defines the application programming model, much like HTML and HTTP define the web application model.
The key components here are:
WML (Wireless Markup Language): A simplified, lightweight version of HTML used to create WAP pages (called "decks").
WMLScript: A scripting language similar to JavaScript, but simpler.

## Slide 91: 2. Session Layer (WSP)
Protocol: Wireless Session Protocol (WSP)
Function: WSP provides two types of session services: connection-oriented (like an HTTPS session) and connection-less (like a single UDP request).
It allows applications to establish, maintain, and terminate a session between the client (phone) and the server.
It's optimized to handle connection interruptions common in wireless networks.

## Slide 92: 3. Transaction Layer (WTP)
Protocol: Wireless Transaction Protocol (WTP)
Function: WTP is the equivalent of a lightweight HTTP. It efficiently handles the reliable transfer of data (transactions) between the client and server.
It offers three types of transaction services (unreliable, reliable one-way, and reliable two-way), but its key feature is its ability to retransmit data reliably without needing the entire TCP overhead.

## Slide 93
Unreliable One-Way Transaction: Data is sent without acknowledgment.
Used when speed is more important than reliability.
Reliable One-Way Transaction: Data is delivered reliably with acknowledgments.
Suitable for requests that do not require a response.
Reliable Two-Way Transaction: Ensures reliable request and response delivery.
Commonly used for client–server interactions.

## Slide 94: 4. Security Layer (WTLS)
Protocol: Wireless Transport Layer Security (WTLS)
Function: This layer is a security protocol based on the industry-standard Transport Layer Security (TLS/SSL).
Its job is to provide data integrity (making sure data hasn't been changed), privacy (encryption), and authentication (verifying identity) for WAP applications.
It is tailored for low-bandwidth networks.

## Slide 95: 5. Transport Layer (WDP)
In the Wireless Application Protocol (WAP) architecture, the Wireless Datagram Protocol (WDP) operates at the Transport Layer.
Its primary purpose is to provide a consistent, unreliable data transport service to the higher layers, regardless of the underlying wireless network technology (bearer) being used.

## Slide 96
Key Functions of WDP
WDP is modeled after the Internet's User Datagram Protocol (UDP) and performs three main tasks:
Port Addressing: Just like UDP, WDP uses 16-bit port numbers to direct data to the correct application or process on the device (e.g., a specific WAP browser session).
Segmentation and Reassembly (SAR): Many wireless bearers (like SMS) have very small maximum packet sizes. If a higher layer sends a large message, WDP breaks it into smaller segments for transmission and reassembles them at the receiving end.
Error Detection (Optional): It can perform basic checksums to detect corrupted data, though it does not provide "reliability" (it won't re-transmit lost packets; that is the job of the WTP layer above it).

## Slide 97: WAP Gateway
Serves as an intermediary between mobile device and the internet.
Functions include:
  Protocol translation (WML ↔ HTML, WTLS ↔ TLS)
  Content adaptation (compressing data for small screens)
  Security management
  Session handling
Converts mobile-friendly requests into web-standard requests and vice versa.
This gateway made it possible for simple mobile devices to access standard web content (in a stripped-down format) without the web servers needing to be radically changed.

## Slide 98: (2G)GSM in Wireless Communication
GSM stands for Global System for Mobile Communication.
It is a digital mobile network commonly utilized by mobile phone users around the world.
It uses 4 different frequency bands 850 MHz, 900 MHz, 1800 MHz, and 1900 MHz.
Conceived in the early 1980s, GSM has grown to become the most widely used mobile communication standard.
It is a circuit switching technology

## Slide 99: GSM Architecture
Its architecture consists of several layers, including the radio interface, network switching subsystem, and operation and support subsystem.
At the core, it enables communication between mobile devices through base stations and network elements.

## Slide 100: Mobile Station (MS)
At the heart of GSM architecture is the Mobile Station (MS), comprising the physical device (phone or modem) and the Subscriber Identity Module (SIM) card.
The SIM card holds vital information, including the user's identity and subscription details, ensuring personalized access to the network.

## Slide 101: Base Station Subsystem (BSS)
The Base Station Subsystem (BSS) is critical in mobile networks, comprising BTS and BSC. It manages signal transmission, ensuring seamless connectivity.
Base Transceiver Station (BTS)
This is the radio equipment that facilitates the transmission and reception of signals.
Base Station Controller (BSC)
The BSC in GSM architecture manages multiple BTS units, optimizing the allocation of radio resources.

## Slide 102: Network Switching Subsystem (NSS)
The Network Switching Subsystem (NSS) is a crucial component in mobile networks, managing call routing and network operations.
Additionally, it ensures seamless communication and efficient resource utilization.
Moreover, the NSS plays a pivotal role in connecting users and facilitating the exchange of information within the telecommunications network.

## Slide 103: Mobile Switching Center (MSC)
The Mobile Switching Center (MSC) is a central component in mobile communication networks that is responsible for call switching and routing.
Furthermore, it acts as a bridge, connecting mobile devices within the network and facilitating seamless communication.

## Slide 104: Home Location Register (HLR)
The Home Location Register (HLR) is a key component in mobile networks, acting as a centralized repository for subscriber information.
Additionally, it stores crucial details such as the subscriber's identity, location, subscription information, and service profile, enabling quick retrieval for seamless call routing and service delivery.
Furthermore, the HLR plays a crucial role in subscriber authentication and authorization, ensuring secure access to network services.

## Slide 105: Visitor Location Register (VLR)
The Visitor Location Register (VLR) complements the Home Location Register (HLR) in mobile networks, managing temporary registration as users move.
Additionally, upon entering a new service area, the VLR interacts with the HLR to retrieve subscriber information, temporarily storing it for efficient call routing and service provisioning.
Furthermore, the VLR facilitates smooth handovers as subscribers roam between network cells, ensuring uninterrupted service delivery.

## Slide 106: Authentication Center (AuC)
The Authentication Center (AUC) in mobile networks safeguards authentication integrity.
Transitioning from the Home Location Register (HLR), generates unique security parameters, securing communication.
Furthermore, the AUC engages in mutual authentication, validating subscriber and network identities.
Additionally, it dynamically verifies credentials, enhancing overall security.

## Slide 107: Operation and Maintenance Center (OMC)
The Operation and Maintenance Center (OMC) is crucial in mobile networks, seamlessly connecting core components like the HLR and AUC.
Moreover, it serves as a centralized hub for monitoring and managing network operations, utilizing tools and protocols to oversee network health and performance.

## Slide 108: General Packet Radio Service (GPRS (2.5G))
GPRS is a packet switching technology that enables data transfer through cellular network GSM, providing end-to-end wide area wireless IP connectivity.